## Slide 1
Access Control & Authentication in ICS
基礎設施安全 第六組

## Slide 2
Problem Definition
In ICS security, lack of authentication is a root cause for many attacks
  Command Injection Attacks
  Response Injection Attacks
  Man-In-The-Middle

## Slide 4
Problem Definition
Most security problems’ root cause is human
  Misbehavior/secret leakage of inexperienced workers
  No access control of who can do what
  Unaccountable behaviors

## Slide 5
Problem Definition
In ICS security, lack of authentication is a root cause for many attacks
  Propose an availability-preserving authentication scheme using MAC and a firewall before PLC
Most security problems’ root cause is human
  Propose an access control scheme using a centralized token-granting server

## Slide 6
Access Control Scheme

## Slide 7
Access Control Scheme
A centralized token-granting server
  Concept borrowed from secure deployment
Token-granting server need to be very secure
  It is assumed trustworthy for the scheme to work

## Slide 8
Access Control Scheme - Advantages
Attacker can’t directly tell HMI what to do even if he can access it
  If HMI is not compromised
Misbehavior of low-privileged employee won’t lead to severe attack
  Secret leakage of a employee who can only control the fan won’t lead to attacker shutting down the factory’s power

## Slide 9
Access Control Scheme - Advantages
Persistent attack is harder
  Tokens expire after a period of time
Incidents are more accountable
Little delay, since users can request their new tokens prior to the token refresh time

## Slide 10
Authentication Scheme - Problems
If attacker can somehow reach the internal network of the PLCs, he can bypass all defenses prior to the HMI
  Since Modbus is a plaintext protocol without authentication functionality
Encryption and decryption between HMI and PLC cause delay and affect availability, which is probably unacceptable
  We don’t actually need encryption for authentication
Use Message Authentication Code (MAC) with pre-installed key!

## Slide 11
Authentication Scheme

## Slide 12
Authentication Scheme
We use MAC for authentication
  The secret key can be pre-installed
  Only a single hash calculation is needed, very efficient
Attacker cannot forge commands without secret key
  Timestamp should be included and checked in payload to avoid replay attack
Unlike decryption, MAC verification can be delayed and separately handled, payload can be immediately forwarded to preserve availability

## Slide 13
Demo

## Slide 14
Conclusion & Discussion
Lack of access control and authentication methods is root cause of many security problems in ICS
We proposed an access control scheme prior to HMI, using a centralized token-granting server
We proposed an authentication scheme between HMI and PLC, using MAC verification
Critical point of failure: token-granting server and HMI

## Slide 15
Q&A